## Slide 1: U-Boot – The Universal Bootloader
Proyecto integrador final – Módulo 3

## Slide 2: Requirements
U-boot v2018.05
  git checkout v2018.05
  am335x_boneblack_defconfig (instead of am335x-evm_defconfig)
TFTP/NFS
  zImage (encoded)
  am335x-boneblack.dtb (decoded)
  nfsroot (decoded)
decode_kernel u-boot command
  3 parameters:
    Memory address where encoded kernel was downloaded
    Memory address to put the decoded kernel
    Cipher KEY

## Slide 3: Requirements
U-boot command should be able to read the data in the “input address”, up to the file size (in bytes)
  File size can be “hardcoded” (fixed value in code)
U-boot command should complain and print the usage string if the argument list is not valid (invalid number of arguments, invalid arguments, etc.)
U-boot command should decode the zImage data starting from the “input address”
U-boot command should place the decoded zImage data in the “output address”

## Slide 4: Requirements
File size is the same in both encoded and decoded zImages
Encoded zImage will be provided. Try to boot that file first to see what happens
The main objective is to:
  TFTP encoded zImage + am335x-boneblack.dtb
  decode_kernel encoded zImage
  Boot decoded zImage + am335x-boneblack.dtb without any errors
  Find out the “special message” hiding in the Kernel boot log

## Slide 5: Coding requirements
Simple XOR cipher
Encoding algorithm
  SIZE = 1 byte
  KEY = 0x10
  0x00 XOR 0x10 => 0x10
  0x01 XOR 0x10 => 0x11
  0x02 XOR 0x10 => 0x12
  0x03 XOR 0x10 => 0x13

## Slide 6: Coding requirements
Simple XOR cipher
Decoding algorithm
  SIZE = 1 byte
  KEY = 0x10
  0x10 XOR 0x10 => 0x00
  0x11 XOR 0x10 => 0x01
  0x12 XOR 0x10 => 0x02
  0x13 XOR 0x10 => 0x03

## Slide 7: Going the extra mile
For example:
What happens if the addresses overlap?